## Slide 1: AI and Machine Learning for IoT Big Data

## Slide 2: Case study 1: WSN

## Slide 3: Wireless Sensor Networks (WSN)
A short review of Wireless Sensor Networks
Anomaly detection in WSN
  Security issues
  Algorithmic approaches
  Clustering approaches
Real-time query processing with Deep Learning

## Slide 4: WSN concepts
Spatially distributed sensors (temperature etc.)
Wireless connections:
    WIFI
    Bluetooth, BLE (short range)
    LoRa, SIGFOX (mid-range)
Streaming data, often low bandwidth
Data protocols, e.g. MQTT

## Slide 5: Example of a WSN: tea field monitoring in Rwanda
Environmental data collected by sensor nodes
Data routed to the Internet and aggregated in the cloud

## Slide 6: A solar-powered WSN node
Credit: https://upload.wikimedia.org/wikipedia/commons/4/48/CSIRO_ScienceImage_3876_A_remote_sensing_node_part_of_CSIROs_Fleck_wireless_sensor_network_technology.jpg

## Slide 7: Other common uses of WSN
Smart city: utilities (e.g. water leakage monitoring), traffic, environment etc.
Intelligent buildings
Health care (e.g. mobile monitoring)
Smart grid
Transport, tracking
Scientific sensing

## Slide 8: WSN anomaly detection
Security issues with smart city WSN
Attack detection: find anomalies
Real-world experiment is difficult
Method: detect simulated anomalies
A Comparative Study of Anomaly Detection Techniques for Smart City Wireless Sensor Networks
Victor Garcia-Font *, Carles Garrigues and Helena Rifà-Pous
http://www.mdpi.com/1424-8220/16/6/868

## Slide 9: Anomaly Detection Methods
Extreme values in Mahalanobis Distance
Local Outlier Factor
Hierarchical Clustering
Classification with Support Vector Machines One-class Support Vector Machines (OC-SVM): Semi-supervised learning with Radial Basis Function (RBF) kernel

## Slide 10: Simulated Smart City WSN
Sound streams collected at 10 locations are reproduced in simulation
http://www.mdpi.com/1424-8220/16/6/868

## Slide 11: Feature Selection
Feature Vector 1 (FV1) : number of application packets, hour of the day
Feature Vector 2 (FV2) : FV1 fields, sequence number, battery level, lost packets, consumed energy
Feature Vector 3 (FV3) : FV2 fields, WSN link quality, received MAC ACK and CTS
http://www.mdpi.com/1424-8220/16/6/868

## Slide 12: Flow of analysis
The anomaly analysis comprises three basic sub-steps for each of the compared techniques: the training, the validation and the test phases.
…The filtered dataset … [is] divided … in Figure. …The attack samples are not included in the training dataset (a), because the detection techniques … are semi-supervised or unsupervised.
… The validation and test datasets … divided into 8 additional datasets ((b) to (i) in the figure), resulting in a total of 17 datasets (16 + 1 training dataset).
http://www.mdpi.com/1424-8220/16/6/868

## Slide 13: Simulated datasets for training the classifier
http://www.mdpi.com/1424-8220/16/6/868

## Slide 14: Training phase
…Normalize and standardize the features in all the datasets (i.e., subtracting the mean and dividing by the standard deviation for each feature), … identify the features that have a zero variance in the training dataset, … removed from the three datasets (i.e., training, validation and test)
… Three different levels of false positive rate: permissive (false positive rate < 15%), restrictive (false positive rate < 10%) and very restrictive (false positive rate < 5%).
http://www.mdpi.com/1424-8220/16/6/868

## Slide 15: Validation and test phase
The validation and test datasets are used to evaluate the performance of the algorithms in 72 experiments: (1 with all the attacks together + 7 with each attack separately) x 3 feature vector definitions x 3 PFPR levels.
..Use the detection algorithms to decide whether each sample has to be considered as an attack or not, …
count the correct identifications of attacks as true positives, the incorrect identifications of attacks as false positives, the correct identifications of no attacks as true negatives and the incorrect identifications of no attacks as false negatives.
http://www.mdpi.com/1424-8220/16/6/868

## Slide 16: Results sorted by True Positive Rate (TPR)
OC-SVM dominates
http://www.mdpi.com/1424-8220/16/6/868

## Slide 17: Discussion
Compare the TPR (True Positive Rate) for the four methods
What is the reason for requiring low FPR (False Positive Rate)? What happens with many false positives?
Consider other anomaly situations; how to weight TPR vs. FPR? When would we allow many false alarms in return for finding all attacks?