## Slide 1: AI and Machine Learning for IoT Big Data

## Slide 2: Case study 3

## Slide 3: Lecture 13: Big Data from Sensors
Case study: Carbon Monoxide Daily Summary
The US EPA CO data on Kaggle
The “Feature engineering” kernel
Exploring the data
Spatial features
Temporal features
Self-study hints

## Slide 4: CO survey by nationwide sensor array
Breathing air with a high concentration of CO reduces the amount of oxygen that can be transported in the blood stream to critical organs like the heart and brain.
https://www.epa.gov/co-pollution/basic-information-about-carbon-monoxide-co-outdoor-air-pollution#Reduce

## Slide 5: EPA CO data on Kaggle
8 million records of curated sensor data
Span: 1994-02-01 to 2017-07-31
Coverage: whole USA (incl. Hawaii)
Contents: CO sensor value (ppm) daily aggregated value daily maximum, its time
Some missing values, errors
https://www.kaggle.com/epa/carbon-monoxide

## Slide 6: Data fields
County Code: The FIPS code of the county in which the monitor resides.
Site Num: A unique number within the county identifying the site.
Parameter Code: The AQS code corresponding to the parameter measured by the monitor.
POC: This is the “Parameter Occurrence Code” used to distinguish different instruments that measure the same parameter at the same site.
Latitude: The monitoring site’s angular distance north of the equator measured in decimal degrees.
Longitude: The monitoring site’s angular distance east of the prime meridian measured in decimal degrees.
Datum: The Datum associated with the Latitude and Longitude measures.
Parameter Name: The name or description assigned in AQS to the parameter measured by the monitor. Parameters may be pollutants or non-pollutants.
https://www.kaggle.com/epa/carbon-monoxide

## Slide 7: Data fields
Sample Duration: The length of time that air passes through the monitoring device before it is analyzed (measured). So, it represents an averaging period in the atmosphere (for example, a 24-hour sample duration draws ambient air over a collection filter for 24 straight hours). For continuous monitors, it can represent an averaging time of many samples (for example, a 1-hour value may be the average of four one-minute samples collected during each quarter of the hour).
Pollutant Standard: A description of the ambient air quality standard rules used to aggregate statistics. (See description at beginning of document.)
Date Local: The calendar date for the summary. All daily summaries are for the local standard day (midnight to midnight) at the monitor.
Units of Measure: The unit of measure for the parameter. QAD always returns data in the standard units for the parameter. Submitters are allowed to report data in any unit and EPA converts to a standard unit so that we may use the data in calculations.City Name: The name of the city where the monitoring site is located. This represents the legal incorporated boundaries of cities and not urban areas.
https://www.kaggle.com/epa/carbon-monoxide

## Slide 8: Data fields
Observation Count: The number of observations (samples) taken during the day.
Observation Percent: The percent representing the number of observations taken with respect to the number scheduled to be taken during the day. This is only calculated for monitors where measurements are required (e.g., only certain parameters).
Arithmetic Mean: The average (arithmetic mean) value for the day.
1st Max Value: The highest value for the day.
1st Max Hour: The hour (on a 24-hour clock) when the highest value for the day (the previous field) was taken.
AQI: The Air Quality Index for the day for the pollutant, if applicable.
Method Code: An internal system code indicating the method (processes, equipment, and protocols) used in gathering and measuring the sample. The method name is in the next column.ted. This represents the legal incorporated boundaries of cities and not urban areas.
https://www.kaggle.com/epa/carbon-monoxide

## Slide 9: Data fields
Method Name: A short description of the processes, equipment, and protocols used in gathering and measuring the sample.
Local Site Name: The name of the site (if any) given by the State, local, or tribal air pollution control agency that operates it.
Address: The approximate street address of the monitoring site.
State Name: The name of the state where the monitoring site is located.
County Name: The name of the county where the monitoring site is located.
City Name: The name of the city where the monitoring site is located. This represents the legal incorporated boundaries of cities and not urban areas.
CBSA Name: The name of the core bases statistical area (metropolitan area) where the monitoring site is located.
Date of Last Change: The date the last time any numeric values in this record were updated in the AQS data system.
https://www.kaggle.com/epa/carbon-monoxide

## Slide 10: The “Feature engineering” Kernel
Kaggle supports datasets and kernels
Kernels are scripts for performing some operation on a dataset
The “EPA CO dataset” has an attached kernel that reads the data, plots it geographically, and starts analyzing it with sklearn
We start from this kernel

## Slide 11: First look at the data with Pandas
Using downloaded and uncompressed local file
Checking data format, statistical distribution of main data item

## Slide 12: What can we do with the data?
Find the range of CO pollution in different years
Pick up more polluted places, plot them
Index the data by date
Plot the polluted areas by years
(next step might be trying to predict next year)

## Slide 13: Areas with pollution over 2 standard deviations
The yearly changes indicate some trend - what is that?

## Slide 14: Self-study hints
Dig deeper! What is the micro-structure, in space and time?
Try finding correlations! What changes together? Why?
Try to find related information! Traffic volumes (place, time) Car emission standard changes